Pre-Construction Conference Check-List

| WCID-17 Inspectors |  | WCID-17 office | (512) 266-1111 |
| --- | --- | --- | --- |
| Juan Sanchez | (512) 801-2966 |  |  |
| Delilah Salinas | (512) 801-4082 |  |  |
| Henry Marley | (512) 748-2868 |  |  |

- District Construction Standards for WCID-17 are online at www.wcid17.org ; be sure to get a current copy and review it.

- Change Orders: submit one copy to the District office and one to the inspector.  If the project is within the City of Lakeway, change orders must also be submitted to Lakeway.  (These copies are in addition to the copies that are going to the engineers).

- Once water and wastewater lines are ready to be laid, a WCID-17 inspector must be notified a minimum of 24 hours prior to start-time.

- No lines will be covered until they have been inspected and passed.

- Erosion controls will be in place and maintained at all times.

- No connections will be made to WCID-17 existing systems unless an inspector is present, or has approved such action.  No water mains will be put in service until the bacteriological samples have passed testing.

- The contractor will immediately report to the inspector any problems encountered or any damage to the existing system.

- In-ground lines shall be protected from dirt and rocks to the maximum extent possible.  Wastewater lines which are connected to lift stations or manholes shall be properly plugged during construction to prevent the entry of water and dirt to any existing wastewater lines.

- Fines:

- Tampering with wastewater manholes, up to a $2,000.00 fine.

- Opening or closing aWCID-17 water valves without a WCID-17 employee present is a $2,000.00 fine.

- Tampering with a fire hydrant is a $2,000.00 fine.

- The contractor is responsible for the quality of workmanship and schedule of work.

- The contractor shall employ only experienced personnel who are familiar with the required work and shall provide full time supervision by a qualified foreman.

ds 10/30/2014